Software for IBS and Radiation
Effects (SIRE) revision summary: testing and improvements

---
SIRE
- Code developed by A. Vivoli (2011)
  - Based on MOCAC (Monte Carlo Code)
  - Scattering angle based on Rutherford cross section
  - Re-written in C
- A revision of the code started in May
  - More flexible and more user friendly (lots of improvement still needed)
  - Flags added (to add flexibility)
  - Aim to make it faster and able to run in parallel (an idea is to implement the module in orbit)

---
About the code
- Input files
  - Twiss file (madx form)
  - Input parameters file (beam characteristics, # macroparticles, # cells (x,z,s), flags)
- Output files
  - New twiss after recurrences
  - Growth rates and emittance evolution file
  - Emittance file (if oneturn)
  - Macroparticle distribution file

---
Structure of the code
1. Reads madx twiss and input parameters files and generates the names of the output files
2. If flag_rec then optimizes the number of points in the lattice to be used in order to speed up the simulation --> Generates new twiss file
3. Generates the distribution of macroparticles given the mean invariants and number of macroparticles and for random phases
4. if the IBSflag=1 then apply the transformation to the momentum frame, then apply the IBS routine in each point of the lattice, transform back to the invariants frame
5. If oneturn=1 the above calculation is done only once and the one-turn emittance evolution around the lattice is written in an output file
6. If oneturn=0 the tracking of the distribution evolution is followed for every element and for each turn for a time TEMPO or until convergence. The mean growth times and mean emittances are calculated and written in an output file every one timestep=TEMPO/NIBSruns (both defined in the input file)
7. If damping=1 and q_ex=1 then the effects of synchrotron radiation damping and quantum excitation are taken into account.

---
The IBS routine
- The distributions are splitted in cells (uniform split with respect to x, z, s)
  - nx, nz, ns (cell numbers) need to be optimized
- Puts the macroparticles in cells and calculates the number of macroparticles and their density in each cell
- Applies the scattering kicks between the macroparticles in each cell (binary collisions) --> redistribution of phase space

---
Ncells optimization - 1turn
- Optimization of ncells (for the CLIC DR)
  - For 100000 macroparticles, a scan was performed in different combinations of nx, nz, ns --> Can we come to conclusion only from 1 turn?
  - Emittance comparison after 1-turn

---
Ncells optimization – 10 turns
- Emittance comparison after 10-turns
- SR is on, QE not debugged yet

---
Ncells optimization – 100 turns

---
# macroparticles optimization
For fixed #cells settings (40,6,1000) the emittance after 10 (right, top), 50 (right, bottom) and 100 (left) turns is calculated --> Optimal number of mp: 60000 (?)

---
Run time Vs #cells
- Different number of cells (nx,nz,ns)
  - For 10 turns (left) and 100 turns (middle)
  - Random initial dist. of 100000 macropart
- Different number of cells (nx,nz,ns)
  - For 10 (middle) and 100 (right) turns
  - Same initial dist. of 100000 macropart

---
Code run time per setting
For 100000 macroparticles, the time of run/cell/mp is calculated for different number of cells (for 10 and 50 turns)
For a good setting of (40,6,1000), the time of run is calculated for different number of macroparticles (for 10 turns)

---
Full simulation with fast option
- The fastrun flag has been added in order to speed up the simulation time
  - The IBS growth time is calculated in 1 turn and assume to be unchanged (or very small variation) within a timestep (or number of turns). The new emittance state is then calculated for this time step considering the above growth time. The timestep is defined from the NIBSruns and the TEMPO from the input parameters file (timestep=TEMPO/NIBSruns)

---
The convergence flag
- Full simulation 400 steps
  - fastrun=1
  - fastrun=0
- Comparison with full time evolution (full & fast)
- Fluctuation around convergence (??)
  - If we use the 1 sigma emittance instead of mean (sum over all)
- Added in the code:
  - If convergence limit achieved, continue until it is achieved for 10 times (valid??)

---
IBS on and off
- Full simulation with fastrun on (400 steps)
- SR on & IBS off
- SR off & IBS on

---
1-turn benchmarking with madx

---
Full simulation benchmarking with madx

---
Energy scan for the CLIC DR

---
Implementation of the module to py-orbit

---
- The growth rates definition is not only IBS (the emittances used are after SR and QE)
- Correct QE (what are the beta functions used? At the end of the lattice?)
- MADX and Piwinski benchmarking (chose the last DR example)
- Energy scan plot with fastrun
- Write the final distribution in file and see the shape
- Take into account phase advance
- What happens to the halo particles?
- What happens to non-G beam distr
- Add Touschek

---
Open issues